# INVITATION TO BID Administrative Information

| INVITATION TO BID Title: | Bid Package 1 |
| --- | --- |
| INVITATION TO BID Project Description: | CNC Equipment (Machine and Lathe) |
| Project Lead: | Josh Svatos, President Regional Technical Education Center 1200 West 21st Street Yankton, SD 57078 Phone: (605) 668-5700 jsvatos@rtecedu.org |
| Submit sealed Bid (if submitting manually): MANUAL BIDS MUST BE RECEIVED AT THE PHYSICAL ADDRESS DESIGNATED FOR COURIER SERVICE AND TIME/DATE STAMPED PRIOR TO THE CLOSING DATE AND TIME. Submit electronically: RFP Site | Regional Technical Education Center 1200 West 21st Street Yankton, SD 57078 Electronic Submission Jsvatos@rtecedu.org City of Yankton http://www.cityofyankton.org/how-do-i-/list-detail-pages/rfp-posts-list-copy |
| Systems for Award Management (SAM) Registration | All vendors/contractors must be registered with the Systems for Award Management (SAM) PRIOR to submitting a bid. You can register online at https://www.sam.gov/portal/SAM/##11. If you are not registered with SAM and need assistance, please call Fred Binder with Planning and Development t District III (605) 665-4408. |
| INVITATION TO BID Closing Date/Time: | 2:00pm CDT June 6, 2016 |
| Bid Opening Time/Date/Place: | 2:00om CDT June 6, 2016 Regional Technical Education Center (RTEC) Board Room |

# PURPOSE

The purpose of this Invitation to Bid (Bid Package 1) is to solicit quotes for the acquisition, delivery, and installation of CNC training equipment; particularly a lathe and mill to be utilized by the Regional Technical Education Center (RTEC) to train students in the field of computer numeric controlled machining systems and robotics technology.

# GENERAL INFORMATION, solicitation instructions and standard terms and conditions

The INVITATION TO BID Lead is the only contact for this Solicitation.  All correspondence regarding this INVITATION TO BID shall be in writing.  In the event that it becomes necessary to revise any part of this INVITATION TO BID, amendments will be posted at the City of Yankton’s RFP website (http://www.cityofyankton.org/how-do-i-/list-detail-pages/rfp-posts-list-copy) .  It is the responsibility of the Bidder to monitor the RFP website for any updates or amendments.  Any personal interpretations or clarifications of this INVITATION TO BID shall not be relied upon.  All changes to this INVITATION TO BID must be in writing and posted at the City’s RFP site to be valid.  Alternate Bids are not allowed.

# INQUIRIES

Questions or other correspondence can be submitted to the Project Lead listed below.

Josh Svatos, President

Regional Technical Education Center

1200 West 21st Street

Yankton, SD 57078

Phone: (605) 668-5700

# SPECIFICATIONS

These specifications are the minimum mandatory specifications that your Bid must meet in order for RTEC to consider your Bid for award.  Restate each specification listed in this section, followed by your response demonstrating that your Bid meets or exceeds the required specifications; provide model, part #, or description, as appropriate.

One (1) Haas TM-1P CNC Tool Room Mill to include the following standard features:

• XYZ travels 30” x 12” x 16” (1016 x 406 x 406 mm)		• 7.5 hp (5.6 kW) Vector Drive

• Tool Load Monitoring 					• Rugged Cast-Iron Construction

• Spindle Air Blast 						• Spindle Speed 6000 rpm

• CT 40-Taper Spindle 						• Tool Release Button

• 3 Spare M-Functions 						• Compact Footprint

• 1-Year Parts and Labor Warranty 				• Full Enclosure

HAAS TM-IP TOOLROOM MILL with Tool Changer

30” x 12” x 16” (762 x 305 x4O6mm), 40 taper, 7.5-hp (5.6kw) vector drive, 6000 rpm, full enclosure, 10-station automatic tool changer, Y and Z-Axis way covers, intuitive programming system, 1 MB program memory, memory lock keyswitch, 15” color LCD monitor, USB port and 5-gallon (57 liter) flood coolant system. Single or three-phase power

The TM-1P shall include the following options:

WIPS-R:		Wireless Intuitive Probing System

Auger:		Chip Auger

CPK-HF:		High Flow Coolant Pump Kit ¾ HP

P-COOL:	Programmable Coolant Nozzle

WL:		Work Light

RTAP-3		Rigid Tapping

Tooling Allowance

Control Simulator Module

ESW-1-Year 1 year extended warranty (2years total)

Shipping to Yankton, SD 57078

One (1) Haas TL-1 CNC Tool Room Lathe to include the following standard features:

• Max Swing 16.00” (406 mm) 			• Tool Load Monitoring

• XZ Travels 8” x 30” (203 mm x 1219 mm) 	• 2 Spare M-Functions

• 7.5 hp (5.6 kW) Vector Drive 			• Compact Footprint

• Spindle Speed 2000 rpm 			• 1 Year Parts and Labor Warranty

• Brushless Servo Motors 			• Haas Visual Quick Code

• Constant Surface Speed (G96) in CNC Mode 	• Intuitive Programming System

Other Features Include:

• Double-anchored baliscrews 			• Direct-coupled servo motors

• High-precision spindle 			• Ribbed castings

HAAS TL-1 CNC/MANUAL TOOLROOM LATHE

16” x 29” (406 x 737 mm) max capacity, 16” (406 mm) swing, 7.5 hp (8.9 kW) vector drive, 2000 rpm, A2-5 spindle, Intuitive Programming System, 1 MB program memory, memory lock keyswitch, 15” color LCD monitor and USB port. No workholding, toolpost, or toolholders included. Operates on single or three-phase power. Enclosure required for CE compliance.

The TL-1 shall include the following options:

MTS:		Manual Tailstock

SR-5:		Manual Steady Rest 5” Max Dia

RTAP-3:		Rigid Tapping

MC8-6:		8” 3-Jaw Scroll Chuck A2-6 Mount

TP 3/4 :		Quick Change Tool post 2 Position

CPK:		Coolant pump Kit

Tooling Allowance

Control Simulator Module

ESW-1-Year 1 year extended warranty (2years total)

Shipping to Yankton SD 57078

# BILLING PROCEDURE

The Contractor must provide a signed invoice upon delivery of each item in this bid package.  The invoice must be submitted no later thirty (30) calendar days after delivery/services were provided.  No invoice will be accepted or paid without receipt of required documentation.  Invoices submitted without the required documentation will be returned to the Contractor for resubmission.

The Contractor must provide the following information with each invoice:

1	Identification of billing period

2	Total amount billed for the billing period

3	Detailed description of services/products provided and associated # of hours/$ amounts, as appropriate

4	Name of authorized individual and contact information for Contractor

Invoices and reports are to be submitted to:

Josh Svatos, President

Regional Technical Education Center

1200 West 21st Street

Yankton, SD 57078

# SUBMISSION REQUIREMENTS

6.1	Required Bid Submission Items

Your Bid Submission must consist of the following:

### Systems for Award Management (SAM) Registration

### All vendors/contractors must be registered with the Systems for Award Management (SAM) either prior to submitting a bid, or before an order is made for the equipment.  You can register online at https://www.sam.gov/portal/SAM/##11.  If you are not registered with SAM and need assistance, please call Fred Binder with Planning and Development t District III (605) 665-4408.

### Bid Schedule

Provide your cost information on Attachment 1, Bid Schedule, below.  Do not submit your Bid on any other form.  Submitting your Bid on a form different than the Bid Schedule may cause your Bid to be rejected as non-responsive.

### Other required response items – Product specification sheets, literature, etc.

6.2	Bid Submission Methods

Bids may be submitted electronically via the City of Yankton’s RFP Website or manually in a sealed envelope/package.  Do not fax or e-mail your Bid.  Your Bid must be received at the Regional Technical Education Center by the date and time specified on the header document.  The official time, for bid closing purposes, is the Regional Technical Education Center’s (RTEC) time clock.

### 6.2.1	Electronic Submission via Yankton RFP Website

If submitting electronically via the City of Yankton’s RFP Website, upload all of the Required Bid Submission Items (See Section 6.1) and enter your cost for each line item; as the “Total Cost” on the Bid Schedule

Upload all competed bid forms in PDF or other readable format such as MS Word or Excel.

### 6.2.2	Manual Submission

If submitting manually (via U.S. Mail, courier or hand-delivery), seal all Required Bid Submission Items in a single envelope or package (be certain to include an original hand-written signature in ink) and label the outside of the package as follows:

Attn: Josh Svatos, RTEC President

Bidder Name: (Company Name)

INVITATION TO BID Title: Bid Package 1

# AWARD

Award will be made to the responsive responsible Bidder with the lowest Total Cost, as provided on the Bid Schedule.  An award is expected to be made on June 10, 2016.

# Installation and Acceptance

Perform complete installation with qualified factory-trained service personnel, including uncrating the shipment and installation of the equipment; provide documentation for all software, as well as an operator’s manual, at the time of delivery, in printed form and/or in electronic form; provide an approved complete set of mechanical and electrical drawings of the equipment (at the time of delivery); in the format requested by RTEC; to assist RTEC staff in maintaining and troubleshooting the CNC mill and lathe equipment; propose an installation and training schedule for RTEC President to review at least 10 days prior to the scheduled delivery of the equipment; define acceptance, especially if testing/implementation is required and/or if the warranty begins upon acceptance.

# Training

The contractor will provide basic training for the CNC mill and lathe equipment upon delivery, or shortly thereafter.

# Warranty, Service and Support, Maintenance, etc.

All equipment shall include 1 year warranty coverage as well as maintenance and support.

# Delivery - Timetable

Equipment should be delivered to the Regional Technical Education Center by August 15, 2016.  If the contractor has any questions about the delivery date, they should contact Josh Svatos, General Manger at 605-668-5700.

INVITATION TO BID; Bid Package 1

# Attachment 1-BID SCHEDULE

This completed Bid Schedule must be submitted with your response.

Haas Tool Room Mill

| Item Number | Item Description | Qty | Cost |
| --- | --- | --- | --- |
| 1 | One (1) Haas TM-1P CNC Tool Room Mill to include the following standard features: |  |  |
|  | XYZ travels 30” x 12” x 16” (1016 x 406 x 406 mm), 7.5 hp (5.6 kW) Vector Drive, Tool Load Monitoring, Rugged Cast-Iron Construction, Spindle Air Blast, Spindle Speed 6000 rpm, CT 40-Taper Spindle, Tool Release Button, 3 Spare M-Functions, Compact Footprint, 1-Year Parts and Labor Warranty Full Enclosure Other Features: 30” x 12” x 16” (762 x 305 x4O6mm), 40 taper, 7.5-hp (5.6kw) vector drive, 6000 rpm, full enclosure, 10-station automatic tool changer, Y and Z-Axis way covers, intuitive programming system, 1 MB program memory, memory lock keyswitch, 15” color LCD monitor, USB port and 5-gallon (57 liter) flood coolant system. Single or three-phase power |  |  |
|  | Machine Cost |  |  |
|  | Option Items |  |  |
| 2 | WIPS-R: Wireless Intuitive Probing System |  |  |
| 3 | Auger: Chip Auger |  |  |
| 4 | CPK-HF: High Flow Coolant Pump Kit ¾ HP |  |  |
| 5 | P-COOL: Programmable Coolant Nozzle |  |  |
| 6 | WL: Work Light |  |  |
| 7 | RTAP-3: Rigid Tapping |  |  |
| 8 | Tooling Allowance |  |  |
| 9 | Control Simulator Module |  |  |
| 10 | ESW-1-Year 1 year extended warranty (2years total) |  |  |
| 11 | Shipping to Yankton, SD 57078 |  |  |
|  | Total Cost |  |  |

Haas Tool Room Lathe

| Item Number | Item Description | Qty | Cost |
| --- | --- | --- | --- |
| 1 | One (1) Haas TL-1 CNC Tool Room Lathe to include the following standard features: |  |  |
|  | Max Swing 16.00” (406 mm), Tool Load Monitoring, XZ Travels 8” x 30” (203 mm x 1219 mm), 2 Spare M-Functions, 7.5 hp (5.6 kW) Vector Drive, Compact Footprint, Spindle Speed 2000 rpm, 1 Year Parts and Labor Warranty, Brushless Servo Motors, Haas Visual Quick Code, Constant Surface Speed (G96) in CNC Mode, Intuitive Programming System Other Features Include: Double-anchored baliscrews, Direct-coupled servo motors, High-precision spindle, Ribbed castings HAAS TL-1 CNC/MANUAL TOOLROOM LATHE 16” x 29” (406 x 737 mm) max capacity, 16” (406 mm) swing, 7.5 hp (8.9 kW) vector drive, 2000 rpm, A2-5 spindle, Intuitive Programming System, 1 MB program memory, memory lock keyswitch, 15” color LCD monitor and USB port. No workholding, toolpost, or toolholders included. Operates on single or three-phase power. Enclosure required for CE compliance. |  |  |
|  | Machine Cost |  |  |
|  | Option Items |  |  |
| 2 | MTS: Manual Tailstock |  |  |
| 3 | SR-5: Manual Steady Rest 5” Max Dia |  |  |
| 4 | RTAP-3: Rigid Tapping |  |  |
| 5 | MC8-6: 8” 3-Jaw Scroll Chuck A2-6 Mount |  |  |
| 6 | TP 3/4 : Quick Change Tool post 2 Position |  |  |
| 7 | CPK: Coolant pump Kit |  |  |
| 8 | Tooling Allowance |  |  |
| 9 | Control Simulator Module |  |  |
| 10 | ESW-1-Year 1 year extended warranty (2years total) |  |  |
| 11 | Shipping to Yankton SD 57078 |  |  |
|  | Total Cost |  |  |
|  | Total – Tool Room Mill and Lathe |  |  |

Please enter the estimated delivery date

assuming an order is made by June 10, 2016:

Company Name of Bidder:

Contact Name/Phone:

Contact E-mail: